News Story

Sensor measures water content in hydraulic fluid,

January 10, 2006 - Designed to continuously monitor hydraulic and lubrication fluids, TestMate™ Water Sensor Model TWS-C measures water content relative to percent saturation of fluid in range of 0-100%, Capacitance sensor absorbs water molecules from fluid and changes capacity value that is directly related to saturation level. Integrated thermoelement on sensor measures temperature of fluid from -13° to 212°F. Temperature and degree of saturation are reported as 4-20 mA signal.

Press Release

Release date: December 22, 2005

Schroeder Industries Presents TestMate™ Water Sensor

Water and Temperature Sensor Continuously Monitors Hydraulic and Lubrication Fluids

Leetsdale, PA- Schroeder Industries, a recognized leader in filtration and fluid conditioning products, introduces the TestMate™ Water Sensor (TWS-C) for continuous monitoring of hydraulic and lubrication fluids. An ideal diagnostic tool, the TWS-C measures water content relative to the percent saturation of the fluid, and ranges from zero (indicating the absence of water) to 100 (indicating 100% water). The TWS-C is ideal for a variety of industries including power generation, pulp and paper, steel, and plastics.

A special capacitance sensor absorbs water molecules from the fluid and changes the capacity value that is directly related to the saturation level of the fluid. An integrated thermoelement on the sensor measure~ the temperature of the fluid in the range of -13o to 212° F (-25o to 100° C). Both this value and the degree of saturation are reported as a 4 to 20 mA signal.

The TWS-C can be directly installed into the hydraulic system with a threaded connection. It is recommended that the sensor be mounted vertically in a known turbulent area with the mechanical connection pointing upwards in hydraulic applications. Additionally, the sensor should be fully submerged with fluid free-flowing around the sensor.

The TWS-C is CE Compliant. A declaration of conformity is available upon request, with relevant EMC standards as EN 61000-6-1, EN 61000-6-2, EN 6:L000-6-3, and EN 61000-6-4.

About Schroeder Industries

Schroeder Industries designs, manufactures and markets filtration products for the fluid p6wer industry. Schroeder is a leader in filtration and fluid conditioning. Their expertise in filtration technology, superior filter and element manufacturing capabilities, dedication to customer service and product support are the reasons Schroeder is considered "The Filter Company.”

For further information about Schroeder Industries and its products, call 724-318-1100 or visit www.schroederindustries.com.

http://news.thomasnet.com/fulIstory/472499/nct